## Slide 1
  How are the various roles of spectrum measurement related and different – pre-allocation, operational use (especially for spectrum sharing), post deployment assessment and enforcement?
Group C

## Slide 2
Attributes | Pre-allocation | Operational Use | Post Deployment | Enforcement
data refresh rate | Months | seconds or subseconds | seconds to months | seconds to days
age of data/latency | Months | miliseconds possibly microseconds depending on architecture | months | seconds to months depending on architecture
Duration of interval required | Months | 10-100 milliseconds to seconds | seconds to months | seconds to years
Spatial scale (Area surveyed) | 100 m to 10 Km | 100 m to 10 Km | 100 m to 10 Km | 100-500 m
Spatial resolution/density | meters to several 100 meters | meters to several 100 meters | meters to several 100 meters | meters to several 100 meters
cost sensitivity per unit | low | high | low | medium to low
directionality | ? | ? | ? | yes
time resolution | seconds or more | seconds or less | seconds or more | seconds or more
frequency resolution | 7.25 Khz - 10 Mhz | 7.25 Khz - 10 Mhz | 7.25 Khz - 10 Mhz | 7.25 Khz - 10 Mhz
receiver sensitivity | depends on primary and sensing architecture | depends on primary and sensing architecture | depends on primary and sensing architecture | depends on primary and sensing architecture
storage capacity | large | very low | large | medium
environmental requirements | non-critical | hardened | non-critical | includes portable outdoor
type of measurement | detailed | simple | detailed | detailed/multiresolution
remote access/integration | desireable | mandatory | desireable | mandatory
calibration across sensors | open problem | open problem | open problem | open problem
on board processing | n/a | depends on cost and architecture | n/a | n/a
dynamic range |  | cost constrained if distributed/ could be less constrained if levereaged service provider architecture |  |