## Slide 1: Dynamic Spectrum Access
Methods, Requirements, and Concerns
Greg Buchwald Motorola Solutions, Inc.

## Slide 2: Database-Enabled Access
Offers greatest protection to incumbents
Requires access to the internet or control channel to query a trusted source database
Current de facto method of choice
  TVWS
  3.55GHz
    Trusted sensing; credentials via database
Excellent for fixed or nomadic access; can present issues for some mobile use-cases
MSI is a proponent of Geo-location Database spectrum access methods and has been a contributor to the art.

## Slide 3: Spectrum Sensing-Enabled Access
On the surface, appears to be the best solution, but:
Issues practical issues can make this difficult
  Hidden nodes
  Protection of RX sites; Receivers don’t radiate (much)
  Generally, must sense below the noise floor to avoid de-sense of incumbent services (time element)
    -132dBm Narrowband emissions
    -118dBm LTE (with many caveats)
    -116dBm TV
MSI fielded an early TVWS sensing system during FCC testing; channel sampling and ranking.

## Slide 4: Making Sensing Work Properly
Multiple system components required
  Network of fixed sensing devices
    Establishes a long term and dynamic database of known waveforms correlated to frequency, location, and temporal behaviors
    Cooperative sensing gain – several papers on the subject
  Augmented by sensing-enabled subscriber / individuals units
    A form of “pay for play”; pay with device use and battery life in return for access
    At a minimum, sense the spectral neighborhood you intend to utilize
    Essentially passive mesh sensing with active feedback to the network of fixed devices

## Slide 5: Concerns
Sensing levels
  Generally into the noise; collaborative
  Dynamic range; IM performance of sensing RX
Waveform ID and spectral characteristics of the DSA signals
  Determine interference threshold and resilience
Hidden nodes / RX-only
  Particularly in P-P cm and mm wave bands
Some services require more protection than others (not my words but in full agreement)
  May not be fixed; may need dynamic rules
Stepping on preamble / headers of signals; response time
Protecting critical infrastructure services

## Slide 6: Something to Ponder
Thank You