## Slide 1
Key Technologies Panel
Milind Buddhikot, Nokia Bell Labs milind.buddhikot@bell-labs.com
April 6, 2016

## Slide 2: Key Projects Panel
Goals:
  Communicate the state of current spectrum measurement efforts.
  Describe the plans for the immediate future (what is in the charted roadmap, and what are the wish list features that you cannot have at this time).
  Identify how these measurements efforts are informing analytical spectrum usage models, and where do such measurement efforts fail)?
Panelists:
  Mike Cotton – NIST ITS
  Preston Marshall – Google
  Greg Buchwald – Motorola Solutions
  Paul Brown – Paradigm4
  Joydeep Acharya – Hitachi

## Slide 3: Spectrum Sensing
Spectrum sensing: Key building block technology for enabling efficient sharing of spectrum in either tiered or peer format
Focus: Tiered sharing with primary (incumbent) and multiple tiers of secondary users
Sensing can be building block for following functions
  Spatio-temporal spectrum usage to access feasibility of sharing
  Primary protection
    Accurate exclusion zone computation
  Tiered spectrum management for secondary use
    Dynamic channel ranking
    Dynamic channel assignment
  Spectrum enforcement via detection of interference that leads to violation of
    Primary protection guarantees
    Secondary channel assignment (exclusivity) guarantees

## Slide 4: Where are we after 10 years?
First wave of spectrum measurement (“observation”) efforts
  Long term measurements in a “space point”
  Successful in making case for potential of sharing
  Providing some key insights into temporal dynamics
First wave of sensing
  Development theory and systems for localized sensors (energy, feature and cyclostationary) for specific bands
  Proofs of need for collaborative sensing
  Limited proofs of usefulness of sensing in addressing limitations of propagation model based spatial exclusion zones (e.g.: in TV whitespace)
De-emphasized as complex, expensive and a deterrent to rapid adoption and success of spectrum sharing

## Slide 5: Way Forward
Leveraging Spectrum Access Server (SAS) based framework to make sensing a critical piece of “practical”, “scalable”, “deployable” sharing
  Collaborative fusion of distributed sensor data at SAS to guide primary protection zone, secondary management and enforcement functions
Issues
  “In-network sensing” : Large number of low-cost, poor, dirty sensors vs. accurate sensors vs. dedicated sensors
  Amount of data -- Collecting meaningful data vs. Junk data
  Shipping data vs. summaries vs. events
  Architecting data processing by exploiting geographical structure (inherently scalable for small spatial scope decisions)
  Limitation of control loop latency --- Time elapse between “Collection of data to epoch of “action” based on that data”.
  “Just right amount of sensing”: How much sensing is enough?
  Sensing for secondary tier co-existence and existence within tiers

## Slide 6: Example of 3.5 GHz End-to-End Architecture
T1
T2
Spatial map Sensor Samples
Operator
RAN SON/EMS Server
Sensing information Sharing API
3
Location 1
Macro Cell
Small Cell with Spectrum Sensor
Location 2
Location 5
Location 3
Location 4
Sensor samples @ Location 5
Cellular Operator
Core
4
2
2-Way API
With Information Obfuscation
Commercial SAS (CSAS)
Internet
Federal
Xmitters
FSS
Earth station
Federal SAS (FSAS)
1
Environment
Sensing Capability (ESC)
Explicit information
Optional
Federal Secure
Network
Chang Wook Kim, Jihoon Ryoo and Milind M. Buddhikot,
“Design and Implementation of an End-to-End Architecture for 3.5 GHz Shared Spectrum,” 7th IEEE BL SAS, Nov 29-Oct 2, 2015.

## Slide 7: Order of Presentations
Mike Cotton – NIST ITS
Preston Marshall – Google
Greg Buchwald – Motorola Solutions
Paul Brown – Paradigm4
Joydeep Acharya – Hitachi

## Slide 8: Questions
Single most important problem in your judgment that community should address
What are the implications of limitations of database technologies on distributed sensor data collection and querying?
Challenges in managing ‘Sea of ordinary sensors’ and resulting data
  Scheduling sensing
  Time constants over which control loop can functions : 10s of secs vs. mins
Basic capabilities in low cost sensors in UE and APs – “can” vs. “should” vs. “will”
Sub-6 GHz spectrum has been focus. cmWave and mmWave present altogether different landscape. Does sensing play role in defining architecture especially when channel widths are large and harmonized spectrum may be small in amount