## Slide 1: Rohde & Schwarz USA, Inc.
NSF Workshop on Spectrum Measurements & Spectrum Management
Randy Neal
System Engineer
San Antonio, TX
randy.neal@rsa.rohde-schwarz.com
COMPANY CONFIDENTIAL

## Slide 2: Introduction to the panelist
Randy Neal
System Engineer
San Antonio, TX
randy.neal@rsa.rohde-schwarz.com
COMPANY CONFIDENTIAL

## Slide 3: Overview
Importance of Receiver Sensitivity
Types of Measurements
  Recordings
  Direction Finding
  Classification
COMPANY CONFIDENTIAL

## Slide 4: Geolocation Technology Considerations Receiver Performance
Anyone who has looked at spectrum in the past years understands it can be bit of the “Wild West” when it comes to what transmitters are doing on air
Many more transmitters on air, and more closely spaced than ever before, and growing more by the day
Any good receiver system has to operate in this environment, and obtain results even for low level signals in the midst of higher power transmitters
COMPANY CONFIDENTIAL

## Slide 5: Geolocation Technology Considerations Receiver Performance: Preselection
The most prominent feature which separates a true receiver from a Spectrum Analyzer is a high performance front end preselection.
  Preselection is a filter system used to block higher power out-of-band signals which would end of over-driving the detection circuits, or cause the receiving system to add attenuation to protect detection circuits, and therefore degrade sensitivity
COMPANY CONFIDENTIAL

## Slide 6: Geolocation Technology Considerations Receiver Performance
When the signal environment is challenging, you need to have a robust instrument for signal acquisition.
For example: a robust receiver in a dense or difficult signal environment can be 10 dB more sensitive than even a high performance spectrum analyzer
  Receiver can therefore be almost 3.5 times further away from signal source!
Not only does it provide for better results (ie, system performance does not impact signal quality), but having a more robust receiving system can improve coverage range for measurements, therefore reducing overall number of sensors needed to cover a given geographic area
`
COMPANY CONFIDENTIAL

## Slide 7: Geolocation Technology Considerations Deployment Economics
How does receiver performance impact deployment considerations
Some basic field testing between different grades of receiver hardware has shown more than 20 db of displayed SNR difference (same signal and setup conditions)
              DF Coverage Results
                5 W transmitter at 2 m height assumed, 10 meter RX antenna height
                No terrain accounted for (i.e. flat ground, roughly 30 km square shown)
COMPANY CONFIDENTIAL

## Slide 8: Measurements: Recording
Can you record? Record what?
  System Independent Measurements (Field Strengths)
  FFT data
  IQ Data
  Mission Data, Audio / Text, Classification Results
  Dumb versus Intelligent Recording
  DF Results
  Geo-Locations
COMPANY CONFIDENTIAL

## Slide 9: Measurements: Direction Finding
Automatic Lines of Bearing
Mobile application able to deal with multipath
Tipping of other measurements
Alarming and storing of Geolocations
COMPANY CONFIDENTIAL

## Slide 10: Measurements: Classification
Spurious Emissions are detrimental for Automatic Detection / Classification Systems
Use 2 types of ways to classify a signal
Conventional – measures signal parameters
Shape Detection – examines only spectral shape
COMPANY CONFIDENTIAL

## Slide 11: Summary
Receiver specs should be considered for environment
  One size does not fit all
Types of signals being detected need to be understood
Efficient and reproducible measurements and reporting structures are key
COMPANY CONFIDENTIAL

## Slide 12: Questions?
COMPANY CONFIDENTIAL